## Slide 1: Proposal for a weighted gradient vector field enabling optimal obstacle avoidance
Presented by: Garrett Clem
Advisor: Jay Wilhelm
Committee: Dr. Bob Williams, Dr. David Casbeer, Dr. Maarten Uijt de Haag

## Slide 2: Introduction
Fixed Wing Unmanned Aerial Vehicles (UAVs)
  Remotely piloted
  On-board flight controller
    Maintain stability
    Carry out mission objectives
Waypoint navigation
  Typically pre-planned at ground station
  May consider known obstacles
  Dynamic obstacles may require waypoint re-planning
Path following
  Connects waypoints with flyable paths
  Least error and control effort achieved with vector field methods

## Slide 3: Problem Statement and Objectives
Problem Statement: Determine vector field weighting functions that enable optimal obstacle avoidance for fixed wing UAVs
Objectives
  Phase 1: Identify specific set of conditions that yields guidance singularity when summing attractive and repulsive GVFs
  Phase 2: Determine GVF weighting functions that improve obstacle avoidance
  Phase 3: Demonstrate GVF obstacle avoidance with ground robot experiments

## Slide 4: Literature Review
Unmanned Aerial System (UAS)
Aircraft
  Fixed wing
  Rotorcraft
Transmitter
Ground Station
Autopilot
  Navigation
  Guidance
  Control
Notes: Unmanned Aerial systems
Fixed wing
Rotorcraft
Autopilot
Navigation, Guidance, and Control
Missions planned at ground station

## Slide 5: Literature Review
Guidance Methods
[Sujit, 2014]
  Guidance provides heading reference commands
  Waypoints, path following
  Accurate and robust to disturbances
  Vector field provided best performance
[Nelson et al., 2005]
  Lyapunov vector field primitives
  Asymptotically approach curve
  Stitch paths together for complex behavior
UAV guidance along path via vector field [Sujit, 2014]
Lyapunov vector field path primitives [Nelson et al, 2005]
Switching primitives guidance for UAV [Nelson et al, 2005]
Notes: Guidance
Provides reference commands to control system

## Slide 6: Literature Review
[Griffiths, 2006]
  Expanded Nelson ‘s method for arbitrary paths
[Frew, 2007a]
  Modify stable field
  Non-linear coordinate transformation
[Frew, 2007b]
  Modify field shape via position estimate covariance matrix
  Standoff tracking uncertain targets
Lyapunov vector field guidance along curved path [Griffiths, 2006]
Non-linear coordinate transformation of stable circular Lyapunov vector field [Frew 2007]

## Slide 7: Literature Review
[Goncalves et al, 2009]
  N-dimensional vector field
  Converge and follows a path
    Static
    Time varying
  Intersection of (n-1) surfaces
  Surfaces defined by implicit functions
    First order partials differentiable
    Bounded second order partials
[Goncalves et al, 2010a]
  Experimental validation (2d,3d robotic systems)
[Goncalves et al, 2010b]
  Stability proofs of vector field

## Slide 8: Literature Review
[Wilhelm et al. 2017]
  Loiter moving target
  Reduced steady-state error in comparison to Lyapunov
  Obstacle Avoidance
    Goal field tracked target ground vehicle
    Repulsive fields representing obstacles
    Fields summed resulting in guidance
GVF and Lyapunov tracking a ground target [Wilhelm et al.]
UAV tracking a ground target and avoiding obstacles [Wilhelm et al.]

## Slide 9: Phase 1 Overview:
Goal:
Objective:
Tasks:
Demonstrate gradient vector field singularities for circular obstacles
Identify specific set of conditions that yields guidance singularity when summing attractive and repulsive GVFs
Build GVF simulation environment
Evaluate scenarios where singularities are expected
Characterize location of singularities

## Slide 10: Phase 2 Overview :
Goal:
Objective:
Tasks:
Determine GVF weighting functions that improve obstacle avoidance
Investigate weighting functions dependent on UAV state
Formulate circulation and convergence weights as functions of UAV state
Determine combination of GVF weights that produces optimal guidance in simulation

## Slide 11: Phase 3 Overview :
Goal:
Objective:
Tasks:
Demonstrate GVF obstacle avoidance with ground robot experiments
Validate modified GVF guidance on mobile robot platform simulating fixed wing constraints
Build differential drive robot
Program robotic framework to take guidance commands
Repeat experiments performed in phase 2 on ground robot

## Slide 12: Success Criteria
Phase 1:
Phase 2:
Phase 3:
Identified location and conditions that cause vector field singularities
GVF weighted functions provide an improved performance over un-modified GVF guidance
Simulation and experimental results are comparable and modified GVF operates in real time

## Slide 13: Thanks
Questions?