## Slide 1: The Impact of Ground Effect on Multi-Rotor VTOL sUAS
Presented By: Gina M. Eberhart
Advisor: Dr. Jay Wilhelm
Committee Members: Dr. Sergio Ulloa, Dr. Robert Williams, Dr. Jim Zhu

## Slide 2: Introduction
Multi-rotor Vertical Take-Off and Landing (VTOL) Small Unmanned Aircraft Systems (sUAS)
Ground Effect
  Aerodynamic perturbations close to ground
  Influences both fixed-wing aircraft and rotorcraft
Multi-rotor VTOL sUAS operating Inside Ground Effect (IGE)
  Flight unstable and unpredictable
Potential ancillary benefits operating IGE:
  Thrust increased IGE
  Required power reduced IGE
Wake compression IGE vs. OGE
(Leishman 2000)
Multi-rotor sUAS hovering close to ground

## Slide 3: Problem Statement and Objectives
Problem Statement: Determine the impact of Ground Effect on flight times for multi-rotor VTOL sUAS
Objectives
  Phase I
    Characterize Ground Effect for sUAS class propeller
  Phase II
    Develop flight time prediction model for sUAS hovering IGE
  Phase III
    Experimentally validate flight time prediction model for sUAS hovering IGE

## Slide 4: Key Findings From Literature
Unmanned Aircraft Systems
  Fixed-wing
  Multi-rotor
  Small UAS
Rotor-Craft Aerodynamics
  Momentum Theory
  Blade Element Theory
  Direction Control
  Turbulence
Fixed-wing aircraft
Multi-rotor aircraft

## Slide 5: Key Findings From Literature
Betz 1937
  Power for constant thrust reduced IGE
  Thrust ratio (TIGE/TOGE)
  Height ratio (z/R)
Knight 1941
  Thrust for three-bladed, flat helicopter rotor increased exponentially IGE
  One rotor diameter
Cheeseman 1955
  Diminishing impact with forward flight
  Empirical definition for thrust ratio
Thrust Curves from Literature

## Slide 6: Key Findings From Literature
Curtis 1984
  Diminishing impact of GE with forward flight
Light 1993
  Exponential thrust curve for helicopter blade using free wake analysis method
Kushleyev 2013 and Powers 2013
  Multi-rotor sUAS
  RPM required to maintain hover IGE reduced
Rotor wake IGE hover, transition, forward flight
(Leishman 2000)
Ground and Ceiling Effect for multi-rotor sUAS
(Kushleyev 2013)

## Slide 7: What Does GE Look Like In Flight?

## Slide 8: Methodology: Phase I
Objective: Characterize Ground Effect for sUAS class propeller
Hardware:
  11 x 7 in sUAS propeller
  Motor and Motor Controller
  Optical Encoder
  Load Cell and Signal Conditioner
  8 Pitot Tubes and Pressure Transducers
  Data Acquisition System
  4 x 8 ft. Particle Board Wall
Testing Parameters:
  Constant power to test stand throughout each test
  Tests conducted for power settings 40-70%
  Ground plane moved to each of 11 distances
  Each distance sampled 3 times at random intervals
  Turbulence intensity measured by pitot tubes
Thrust test rig instrumentation

## Slide 9: Methodology: Phase II
Objective: Develop flight time prediction model for sUAS hovering IGE
Hardware Parameters:
  3D Robotics IRIS assumed
  3-Cell 8C 5100 mAh Lithium-Polymer Battery
Model Development:
  Height modeled as step input
  Thrust during hover equal to weight of vehicle
  Power during hover at known height ratio from Phase I data
  Flight time in minutes
    C= Capacity of battery
    Id= Current draw at desired power setting
3D Robotics IRIS at hover
(https://www.dronomag.com/15-best-drones-for-aerial-photography-2/)

## Slide 10: Methodology: Phase III
Objective: Experimentally validate flight time prediction model for sUAS hovering IGE
Hardware Parameters:
  3D Robotics IRIS assumed for flight parameters
  3-Cell 8C 5100 mAh Lithium-Polymer Battery
  Vicon motion capture hardware and software
  Power Sensor
  Pixhawk Flight Controller
Flight Testing Parameters:
  Conducted indoors
  Vehicle will operate until hover can no longer be maintained
  Flight time and power draw monitored
  Comparison with Phase II flight time prediction model
Pixhawk flight controller on IRIS quad-copter

## Slide 11: Success Criteria
Phase I
  Establish relationship for thrust ratio versus height ratio for sUAS propeller at power settings from 40-70% of max power and height ratios between 0.1 and 6.5
Phase II
  Flight times prediction model compares to expected flight times based on specifications of 3DR IRIS within 10% OGE and can be used to predict impact of flight close to ground
Phase III
  Able to measure flight times and discern impact of flight close to ground

## Slide 12: Expected Deliverables
Phase I
  Conference Paper
    Eberhart, G. M., & Wilhelm, J. (2017). Impact of Varied Power Setting on Thrust of Multi-Rotor VTOL sUAS in Ground Effect. In AIAA Information Systems-AIAA Infotech@ Aerospace (p. 0226).
Phase III
  Final thesis document
  Journal submission detailing results of Phases I-III
    AIAA Journal of Guidance, Control, and Dynamics
    Unmanned Systems (World Scientific)
Package Delivery by sUAS
(Ulrich Baumgarten via Getty Image)

## Slide 13: Project Timeline
Thrust and turbulence intensity data collection for select power settings and distances IGE and OGE complete
Flight time prediction algorithm for multi-rotor sUAS hovering IGE and OGE complete
Flight testing experimental setup complete
Experimental data collection for quad-rotor hovering IGE and OGE complete
Thesis document complete
Journal article complete and submitted

## Slide 14: Thank You, Questions?

## Slide 15: Addendum: TR vs. HR
Fit Constant | Value
a | 0.0974
b | -1.935
c | 1.007
d | -0.00049
Experimental Thrust Ratio versus Height Ratio

## Slide 16: Addendum: Comparison with Literature
Thrust Ratio comparison with literature

## Slide 17: Addendum: Power, Thrust, HR Contour
Absolut thrust mapping

## Slide 18: Addendum: Additional Images Thrust Rig
11 x 7 inch sUAS class propeller
Thrust test rig

## Slide 19: Addendum: Wake Rake
Pitot tube wake rake