## Slide 1: Thesis defense: An optimized circulating vector field obstacle avoidance guidance for unmanned aerial vehicles
Presented by: Garrett Clem
Advisor: Dr. Jay Wilhelm
Committee: Dr. Bob Williams, Dr. David Casbeer, Dr. Maarten Uijt de Haag
Notes: Getting started
Refreshments available
Thank audience for attending, thanks to committee (Dr. Casbeer for traveling)
Introduction to fixed wings
Problem statement /objectives
Literature review – motivated the problem statement
Phases
Timeline
Questions

## Slide 2: Introduction
Fixed Wing Unmanned Aerial Vehicles (UAVs)
  Remotely piloted
  On-board flight controller
    Maintain stability
    Carry out mission objectives
    Follow waypoints or ground track
Waypoint navigation
  Typically pre-planned at ground station
  May consider known obstacles
  Unknown obstacles may require waypoint re-planning
Sequential pre-planned waypoints
Hand-launched fixed wing UAV
Gradient vector field [ Goncalves, 2010]
Notes: Fixed wing UAVs are a category of robotic aircraft
Remotely piloted with the assistance of an on-board autopilot
Autopilot maintains vehicle stability
Carry out mission objectives such as following waypoints
Waypoints are typically pre-planned before flight at a ground station
Obstacles such as buildings, mountains, and general no-fly zones may be considered during planning
During flight, unknown obstacles may be encountered which could require waypoints to be re-planned.
The UAV typically communicates with a ground station over radio to plan waypoints which may not always be possible
A possible solution is to use vector field guidance which combines path following with obstacle avoidance

## Slide 3: Problem Statement and Objectives
Problem Statement: Utilize vector field guidance to enable optimal obstacle avoidance without re-planning waypoints
  Phase 1: Identify specific set of conditions that yield guidance singularity when summing attractive and repulsive GVFs
  Phase 2: Determine GVF weighting functions that improve obstacle avoidance
  Phase 3: Demonstrate GVF obstacle avoidance with crazyflie quadcopter under Dubin’s turn rate constraints
Straight path vector field guidance with obstacle
Notes: Problem statement
Guidance between waypoints produced by an attractive vector field that has both circulation and convergence components
Obstacle along the path detected after planning can be represented as a repulsive field
Summing together fields can result in singularities
This will be achieved by completing three phases. (execution of three phases)
Phase 1: Description
Phase 2: Description
Phase 3: Description

## Slide 4: Literature Review
Unmanned Aerial System (UAS)
Aircraft
  Fixed wing
  Rotorcraft
Radio /Transmitter
Ground Station
Autopilot
  Navigation
  Guidance
  Control
Notes: UAVs are a part of a larger system called an Unmanned Aerial System which typically consists of four parts
The physical aircraft itself which typically can be categorized under one of two categories consisting of fixed wing and rotorcraft
Fixed wing UAVs typically have a larger payload and can fly long endurance missions compared to rotor craft
Rotor craft are more maneuverable and do not require a runway or launcher for deployment
Transmitters are used for direct UAV control and can be used short range
Radios can be used for long distance communication and for relaying sensor data back to a ground station
Ground stations are typically a PC equipped with software that sets vehicle parameters, collects data, and plans mission waypoints
Mission waypoints can be communicated back through the radio and sent to the autopilot which uses GNC systems to fly from waypoint to waypoint
Navigation consists of measuring the UAV state which is fed to G and C
Path, or waypoints, are fed to guidance which typically outputs a desired heading to the guidance system which actuates the UAVs controls to transition to the desired state
Guidance is where vector fields comes in

## Slide 5: Literature Review
Guidance Methods
[Sujit, 2014]
  Guidance provides heading reference commands
  Waypoints, path following
  Accurate and robust to disturbances
  Vector field provided best performance
[Nelson, 2005]
  Lyapunov vector field primitives
  Asymptotically approach curve
  Stitch paths together for complex behavior
UAV guidance along path via vector field [Sujit, 2014]
Lyapunov vector field path primitives [Nelson, 2005]
Switching primitives guidance for UAV [Nelson, 2005]
Notes: Sujit et al presented a comparison between five common heading based guidance techniques (Carrot chasing, NLGL, PLOS, LQR, and Vector Field)
Guidance must be accurate (low error) and robust (rejects disturbances)
Guidance methods can fall under either waypoint or path following methods
Monty Carlo simulation of the five guidance techniques involving external wind disturbances determined that the path following vector field method had a low cross track error and was robust to external wind disturbances
Which is important for small fixed wing UAVs since winds can be expected to be 20-30% of the UAVs air speed
Nelson et al. demonstrated the construction of a lyapunov vector field for straight line a circular path primitives, which can be shown in the two figures at the bottom
The robustness of vector field is due to the converging nature of the field followed by circulation. Deviation from the path results in guidance back onto the path.
Nelson combined the use of straight line and circular primitives together to form more complex flight paths, shown in this figure
- The difficulty in using path primitives is the transition from one field to another

## Slide 6: Literature Review
[Griffiths, 2006]
  Expanded Nelson ‘s method for arbitrary paths
[Frew, 2007a]
  Modify existing field
  Non-linear coordinate transformation
[Frew, 2007b]
  Modify field shape via position estimate covariance matrix
  Standoff tracking uncertain targets
Lyapunov vector field guidance along curved path [Griffiths, 2006]
Non-linear coordinate transformation of stable circular Lyapunov vector field [Frew 2007]
Notes: - Griffiths expanded on Neslon’s method and provided a lyapunov vector field for an arbitrary path, which is shown in the figure above
For closed paths, such as a loiter, Frew modified an existing circular field with non-linear coordinate transformation to produce a racetrack and elliptical pattern
Beneficial because fields already proven to converge
In the later paper, the vector field was used for tracking an uncertain target. The field was modified based on a kalman filters covariance matrix

## Slide 7: Literature Review
[Goncalves, 2009]
  N-dimensional vector field
  Converge and follows a path
    Static
    Time varying
  Intersection of (n-1) surfaces
  Surfaces defined by implicit functions
    First order partials differentiable
    Bounded second order partials
[Goncalves, 2010a]
  Experimental validation (2d,3d robotic systems)
[Goncalves , 2010b]
  Stability proofs of vector field
VF
Process
VF
Process
Circular vector field converging at intersection of surfaces
Straight path vector field converging at intersection of surfaces
Notes: Goncalves et al presented a method for constructing an n-dimensional vector field that is guaranteed to converge and follow both static and time varying paths
Field circulate and converge at the intersection of (n-1) surfaces defined by implicit functions that must:
Have first order partials
Bounded second order partial derivatives
A vector field that converges and follows a straight line can be produced by intersecting two planes, shown above
And a vector field that converges and follows a circular path can be produced by intersecting a cylinder and a plane
Fields contain three components
Convergence
Circulation
Time varying
Other papers

## Slide 8: Literature Review
Normalized Convergence Normalized Circulation Total Field
Notes: Goncalves et al presented a method for constructing an n-dimensional vector field that is guaranteed to converge and follow both static and time varying paths
Field circulate and converge at the intersection of (n-1) surfaces defined by implicit functions that must:
Have first order partials
Bounded second order partial derivatives
A vector field that converges and follows a straight line can be produced by intersecting two planes, shown above
And a vector field that converges and follows a circular path can be produced by intersecting a cylinder and a plane
Fields contain three components
Convergence
Circulation
Time varying
Other papers

## Slide 9: Literature Review
[Wilhelm et al. 2017]
  Loiter moving target
  Reduced steady-state error in comparison to Lyapunov
  Obstacle Avoidance
    Goal field tracked target ground vehicle
    Repulsive fields representing obstacles
    Fields summed resulting in guidance
    Did not consider circulation to improve obstacle avoidance
    Did not address singularities
GVF and Lyapunov tracking a ground target [Wilhelm et al.]
UAV tracking a ground target and avoiding obstacles [Wilhelm et al.]
Notes: Wilhelm et al. attached a circular gradient vector field to a moving ground target resulting in a low tracking error loiter
In comparison to lyapunov vector fields by [NAME]
Obstacles were added to the simulation by placing a vector field with a negative convergence near the vehicles path
Summing together attractive loiter field and obstacle field produced a heading guidance which loitered the vehicle while avoiding obstacles
Obstacle fields only considered repulsive vectors and had zero circulation.
Summing vector fields could produce singularities where guidance vanishes (or singularity)
Discuss the three phases:

## Slide 10: Methodology Overview
Phase I:
  Objective: Characterize and present a method for locating singularities in a summed GVF
    Construct field from literature
    Evaluate scenarios where singularities are expected
    Characterize location of singularities
Phase II:
  Objective: Determine a combination of circulation and decay radius for circular obstacle GVF for optimized avoidance
    Define obstacles in terms of UAV radius
    Determine radius and circulation for optimized avoidance
Phase III:
  Objective: Demonstrate optimized GVF guidance on multirotor UAV flying with turn rate constraints
    Build quadcopter and modify for external commands
    Program optimized guidance and control framework
    Conduct flight tests and compare to simulations
Summed GVF magnitude surface with singularity
Optimized avoidance path
Crazyflie quadcopter

## Slide 11: Phase I: GVF singularity detection
  Objective: Characterize and present a method for locating singularities in a summed GVF
  Construct path following and obstacle fields
  Sum fields and weight repulsive field
  Determine radius where fields have equal strength
  Observe vector lengths in summed field
  Singularities expected on radius of equal strength
Singularity Condition
Guidance

## Slide 12: Phase I: GVF singularity detection continued
  Objective: Characterize and present a method for locating singularities in a summed GVF
  Two methods for locating singularities in a summed GVF
    1) Brute force, evaluate region around obstacle and identify any minimums
    2) Numerically search for singularity with initial conditions placed on radius of equal strength
  Adding circulation to field removes singularities from UAVs route
  Circulation removes directly opposing vectors that cancel

## Slide 13: Phase II: Obstacle field optimization
  Objective: Determine a combination of circulation and decay radius for circular obstacle GVF for optimized avoidance
  Demonstrate Dubin’s vehicle simulating fixed wing UAV guided by GVF
  Path following field circulation
  Define obstacle in terms of UAV turning radius
  Cost function to measure path deviation
  Demonstrate avoidance for strictly repulsive GVF centered on path

## Slide 14: Phase II: Obstacle field optimization
  Objective: Determine a combination of circulation and decay radius for circular obstacle GVF for optimized avoidance
  Worst case head on collision scenario
  Strictly repulsive field
  Iteratively increased k until avoidance was achieved
  Singularities along path
  Excess path deviation
  Unnecessary turns
  Slow return to planned path

## Slide 15: Phase II: Obstacle field optimization
Optimized
Brute force and equal magnitude convergence an circulation

## Slide 16: Phase III: Implement GVF on crazyflie
  Objective: Demonstrate optimized GVF guidance on multirotor UAV flying with turn rate constraints
  Program optimized GVF guidance and PID controllers in python
  Validate python and MATLAB identical
  Compare simulation and experimental flight costs

## Slide 17: Results: Phase I & II
  Objectives
  Phase I: Determine a combination of circulation and decay radius for circular obstacle GVF for optimized avoidance
  Phase II: Characterize and present a method for locating singularities in a summed GVF
  Four scenarios evaluated
    Centered, off centered
    Small radius, large radius

## Slide 18: Results: Phase I & II
  Objectives
  Phase I: Determine a combination of circulation and decay radius for circular obstacle GVF for optimized avoidance
  Phase II: Characterize and present a method for locating singularities in a summed GVF
  Four scenarios evaluated
    Centered, off centered
    Small radius, large radius

## Slide 19: Results: Phase I & II

## Slide 20: Results: Phase III
Objective: Demonstrate optimized GVF guidance on multirotor UAV flying with turn rate constraints
Compare experimental cost and simulation cost for 4 scenarios
Centered
Off centered
Small radius
m=1.5 radius

## Slide 21: Results: Phase III

## Slide 22: Results: Phase III

## Slide 23: Results: Phase III

## Slide 24: Results: Phase III

## Slide 25: Results Summary
Phase I:
  Objective: Characterize and present a method for locating singularities in a summed GVF
Phase II:
  Objective: Determine a combination of circulation and decay radius for circular obstacle GVF for optimized avoidance
Phase III:
  Objective: Demonstrate optimized GVF guidance on multirotor UAV flying with turn rate constraints

## Slide 26: Conclusions
Singularities in GVF can be found by searching for zero vector lengths numerically with equal strength initial conditions
Circulation removes singularities from path preventing tap situation and null guidance
Decay radius R and circulation H may be optimized for avoidance by minimizing path deviation cost function
Optimized GVF performs similar to waypoint and better than unmodified GVF or VFF
GVF can be implemented for real time guidance, as demonstrated with multirotor flight experiments

## Slide 27: Thanks
Questions?